## Slide 1
SEVERN EDGE AI
Today, YOU teach a robot
Arduino Nano 33 BLE
Your board learns gestures from your data
Connect
Collect
Train
Test
Notes: Hook: 'Is AI magic?'
This board will learn from students today.
Set expectation for workflow: Connect -> Collect -> Train -> Test.

## Slide 2
How the Sensor Captures Your Move
IMU sensor
ax (left-right)
az (up-down)
ay (forward-back)
gx (rotation)
gy (rotation)
gz (rotation)
ax (left-right)
ay (forward-back)
az (up-down)
gx (rotation)
gy (rotation)
gz (rotation)
Notes: Students see 6 sensor channels in real time.
Red axes are acceleration (ax, ay, az); blue axes are rotation (gx, gy, gz).
Main teaching line: AI does not see motion directly, only these changing numbers.
Use the 3x2 card grid to ask: which channels change most for each movement?

## Slide 3
What the AI Actually Sees
100 time steps x 6 axes = 600 numbers
ax
ay
az
gx
gy
gz
low
high
Wave
Shake
Notes: Say this slowly: each gesture recording is 100 readings x 6 numbers = 600 numbers.
Point to bottom heatmaps: Wave and Shake look like different number patterns.
This is the core insight before students begin collecting data.

## Slide 4
CHALLENGE TIME!
Can your AI score 7 out of 10?
7/10
Goal: at least 7 correct attempts
1
See the target gesture
2
Do the move
3
Tap Score Attempt
Notes: Set the game target: 7 out of 10.
Students should wait until predicted label matches before scoring each attempt.
Focus: model quality comes from consistent movement and clear gesture differences.

## Slide 5
YOU JUST TRAINED A REAL NEURAL NETWORK!
GOOD DATA
=
GOOD AI
DIFFERENT
PATTERNS HELP
MORE PRACTICE,
BETTER RESULTS
AI IS MATH,
NOT MAGIC
Same idea, different scale
YOU TODAY
30 samples
6 sensors, 1 Arduino
REAL AI
Millions of samples
Hundreds of sensors
Notes: Celebrate achievement first.
Recap the 4 lessons from class.
Close with transfer idea: same ML principles scale to robotics and self-driving systems.